## Slide 1: WiFi Introduction
2022/07/14

## Slide 2: OSI Model Layers
MAC
PHY

## Slide 3: 802.11 Standards
802.11
802.11a
802.11b
802.11g
802.11n
802.11ac
802.11ax
802.11be
...

## Slide 4: 802.11a
max 54Mbps
  OFDM
  6, 9, 12, 18, 24, 36, 48 & 54M
works @ 5G band

## Slide 5: 802.11b
max 11Mbps
  DSSS
  1, 2, 5.5, 11Mbps Rate
works @ 2.4G

## Slide 6: 802.11g
54Mbps
  OFDM
  6, 9, 12, 18, 24, 36, 48 & 54M
compatible with 802.11b

## Slide 7: 802.11n
max 600Mbps
2.4G and 5G band
OFDM
Features:
  More subcarriers
  Coding Rate
  Short GI
  40M bandwidth
  MIMO (with 4 SS) and beamforming
  AMSDU and AMPDU
  BlockACK

## Slide 8: 802.11ac
works @ 5G band
160M bandwidth
MIMO * 8
256 QAM

## Slide 9: 802.11a/b/g/n/ac

## Slide 10: 802.11 Basics
SSID: Service Set Identifier
BSSID: Basic Service Set Identifier
BSA: Basic Service Area
ESS: Extended Service Set

## Slide 11: 802.11 Frame

## Slide 12: 802.11 Frame - Frame Control

## Slide 13: 802.11 Frame - Duration/ID

## Slide 14: 802.11 Frame - Addresses
Indicate the BSSID, SA, DA, TA (Transmitter address), RA (Receiver address), each of 48-bit address.

## Slide 15: 802.11 Frame - Seq control
  Sequence Number (12-bit): An incrementing value. The same value shall be used for all fragments of the same MSDU.
  Fragment Number (4-bit): Indicates the number of each individual fragment.

## Slide 16: 802.11 Frame Types
Data Frame
Control Frame
  RTS, CTS, PS-POLL, BAR, BA, Trigger Frame, etc.
Mgmt Frame
  beacon
  assoc/auth/deauth/action, etc.

## Slide 17: Data Frames

## Slide 18: Frame exchange sequences
The following frame sequences are possible:
  Data
  Data - ACK
  RTS - CTS - Data - ACK
  Data - ACK - Data - ACK (Fragmented MSDU)
  RTS - CTS - Data - ACK - Data - ACK (Fragmented MSDU)
  ...

## Slide 19: Management Frames
Management Frames
  The BSSID
    The AP address, if the station is an AP or associated with an AP.
    The BSS ID of the ad hoc LAN, if the station is a member of an ad hoc LAN.
  The Frame body shall be the information elements:

## Slide 20: Management Frames - Information Element

## Slide 21: How to connect to AP
Scan
Authentication and PMK Caching
Association or FILS Assoc
DHCP/DHCPv6, etc.

## Slide 22: Scan
Active Scan
Passive Scan

## Slide 23: Authentication
Shared Key
Open System
SAE
802.1X

## Slide 24: Association
Negotiate MAC/PHY capabilities
ciphers: TKIP, CCMP, GCMP, etc.

## Slide 25: WPA/WPA2/WPA3 4-way handshake

## Slide 26: WiFi SDK 3.0.X structure
ip: 802.11 stack
wpa_supplicant: mlme, sme
rwnx_intf: data path and mgmt path
lwip: tcp/ip protocol stack
wlan_ui/wlan_cli: WiFi API
wolfssl/mbedtls: 3rdparty crypto routine for SHA-1, SHA-256, DH, ECC, etc.
How to review code?
WIFI API -> MGMT -> macsw
LWIP API -> DATA -> macsw

## Slide 27: Basic WiFi API
bk_wlan_start: start STA/softAP
bk_wlan_start_p2p: start P2P
bk_wlan_stop: stop STA/softAP
bk_wlan_start_scan: scan AP
bk_wlan_start_monitor: monitor mode
bk_wlan_stop_monitor: stop monitor mode
sta_ip_start: assign static IP or start DHCPC

## Slide 28: How to capture WiFi packets
Omnipeak for Windows
Wireshark for MacOS
  set adapter mode to radiotap
Wireshark for Linux
  set adapter to monitor mode, for example
  ifconfig wlan0 down
  iw wlan0 set mode monitor
  ifconfig wlan0 up

## Slide 29: Task to Do
wpa_supplicant / hostapd new features
  DPP
  802.11k
  802.11v
  WPA3
  ...
macsw
  data path
  mgmt path
  stability
  perfomance

## Slide 30: Books recommended
802.11: The definitive Guide 中文版 《802.11权威指南》
802.11n: The survival Guide
802.11ac: The survival Guide
CWNA
Wi-Fi 6 for dummies
Wi-Fi 6 Protocol And Network
Advanced:
Next Generation Wireless LANs 802.11ac
802.11 Spec.
Others:
Matlab 802.11 Toolbox for PHY study
Linux mac80211

## Slide 31: Next Lecture
802.11 In Details (in 3-4months)
wpa_supplicant/hostapd
802.11 PHY
802.11 MAC Layer
802.11 Security